## Slide 1: Radiation Environment in Space
Luisa Arruda
luisa@lip.pt

## Slide 2
Space Radiation Environment
Van Allen
Radiation Belts
Galactic Cosmic
Radiation (GCR)
Protons and electrons
AP-8 and AE-8 models
p, , O and Fe
ISO 15390
Solar min: 30 Jan 2009
Solar max: 30 Jan 2014
1 AU from Earth
SEP event
Protons
Integrated 14 day SEP event of December 2006

## Slide 3: Solar Wind
Continuous flux of charged particles from the Sun ~400km/s
  mainly e- and p (E~0.5MeV)
  ~1012 particles/m2.s
~4 days to reach the Earth (1UA).
First continuous observation by spacecraft Mariner 2 (1962).
Detailed measurement by spacecraft Ulysses (3 orbits).
“Swepts” the solar magnetic field to IP space

## Slide 4: Solar Magnetic Field
α
α
Sun rotation period ~27.26 days
( Carrington rotation – started 9 Nov 1853)
Magnetic field and magnetic poles approach a dipole.
Continuous Shift between the Sun rotation axis and the magnetic field direction when solar activity comes from Min to Max.
Complex configuration during Solar Max.
Polarity reverses each 11 yrs, returning to its original configuration every 22 years

## Slide 5: Indicadores de Actividade Solar
Monitores de neutrões
✔ RC primários (protões) interagem com a atmosfera e produzem neutrões secundários
✔ Monitores de neutrões situados a diferentes altitudes e latitudes medem esta componente
✔ detecção por tubos proporcionais rodeados de materiais de elevado-Z (Pb) e baixo-Z (plástico) para amplificar a componente secundária de neutrões e fazer escudo à radioactividade de fundo.
✔ Medidas da taxa de neutrões dá informação da variação da intensidade de RC.
Sunspots
✔ número de manchas solares (regiões + frias que a fotoesfera à volta) monitorizam a actividade Solar
✔ podem ser tão extensas como 105 Km
✔ periodicidade de 11 anos
✔ ciclo solar: de um mínimo ao próximo (1º ciclo : 1755-1766)

## Slide 6: GCR and Solar cycle activity
Modulation with solar activity – 11 yr cycle
Solar cycle modulated flux inversely proportional to the Sun’s activity
Maximum: solar storms and SEP
Minimum: more GCR
α
https://www.swpc.noaa.gov/products/solar-cycle-progression

## Slide 7: Solar Cycles

## Slide 8: SEP – Solar energetic particles
Associated to
Solar flare
Coronal mass ejections (CME)
Mainly protons and electrons
Energies from several hundred MeV/nuc to GeV/nuc
List from 1976-present @ https://umbra.nascom.nasa.gov/SEP
At Earth's surface, the atmosphere in conjunction with the geomagnetic field provides considerable protection against cosmic rays and solar particle events!
In Space, SEPs are responsible for spacecraft system and component hazard and damage and impose strict constrains on human space exploration.

## Slide 9: SEP - Eventos solares

## Slide 10
Solar Energetic Particle Events
Long term record
More in “maximum” solar activity years
Highly unpredictable
Design for by making a statistical assessment

## Slide 11: The Magnetosphere: an invisible shield
Particles coming from space and produced in their interaction with the atmosphere are trapped by the Earth’s magnetosphere forming the Earth´s radiation belts
In Earth orbits the radiation belts containing trapped electrons and protons constitute the major radiation source

## Slide 12: Earth radiation belts
Particles coming from Space depending on their R may be trapped by the geomagnetic field and form the Earth’s radiation belts.
In Earth’s orbits the radiation belts containing trapped e- and p constitute the major radiation source = dynamic environment
Inner belt (700-10000km)
Dominated by p
Product of CR Neutron Decay
E~100’s MeV
Outer belt (~20000-70000km)
    Dominated by e-
    Controlled by “storms”
Dominates GEO environment & Navigation (Galileo, GPS) orbits & certain Science missions in highly elliptic orbits (XMM-Newton, INTEGRAL)
    E~ MeV

## Slide 13: Earth Radiation Belt Models
protons
Based on data from 1960-1970
Long term averages
but : outer belt is very stormy
ongoing work to update models
Electrons
ISS
Nav
GEO
Examples of models: AP8, AE8 (but there are more…)
electrons

## Slide 14: Aurora
The charged particles trapped in the radiation belts may excite the Earth’s atmosphere N2 and O2 that when return to the fundamental state emit visible radiation.

## Slide 15: South Atlantic Anomally

## Slide 16: Radiation effects in Earth orbits

## Slide 17: Radiation environment in the Solar system
Courtesy of Eamonn Daly, ESA

## Slide 18
The Moon

## Slide 19: The Moon
No Atmosphere
Very weak localized crustal magnetic field
Radiation environment
SEP and GCR @ 1AU
Albedo neutrons (modulated by H2O)
No radiation belts
Measured Neutron spectra
(Lunar Prospector)
Radiation environment: similar to Mars
Notes: 0.025–0.4 eV

## Slide 20: Apollo Programme – Solar Maximum
~ 40 Sv acute skin dose (without shielding) from August 72 SPE. Potentially very serious for the lander/EVA
20 mSv annual limit for radiation workers on Earth
~ 2.4 mSv annual dose from natural sources on Earth
0.5 Sv annual limit for ISS astronauts
1Sv = 1 J/kg
== absorbed dose in Gray for
x- rays, gamma rays, beta particles, muons
x Q factor for neutrons, protons, pions and nuclei
1 unit of dose equivalent (the biological effect of ionizing radiation), equal to an effective dose of a joule of energy per kilogram of recipient mass.

## Slide 21: Mars
Away from home

## Slide 22
Mars Radiation Environment
Corresponds to proton range on Mars atmosphere
Spectral
changes

## Slide 23
Radiation Environment Modelling
23
MarsREM: the Mars Energetic Radiation Environment Models
LIP developed dMEREM, a Geant4 based model for the radiation environment on Mars, Phobos and Deimos, including local treatment of surface topography and composition, atmospheric composition and density (including diurnal + annual variations) and local magnetic fields.
Example of dMEREM results:
Particle radiation arriving on Mars surface after GCR-alpha interaction with atmosphere and soil
Inputs given as a function of latitude, longitude, in a 5º x 5º grid, and season.

## Slide 24
Validation of dMEREM, the Detailed Mars Energetic Radiation Environment Model, with RAD Data from the Surface of Mars
Protons at the surface of Mars September 2017
Protons at the surface of Mars Nov 2015 – Jan 2016
P. Gonçalves L. Arruda, M. Pinto, , Front. Astron. Space Sci., 21 February 2022, Sec. Planetary Science

## Slide 25: 30 days on Mars
Mars location | Ambient Dose Equivalent (mSv)
Viking 1/Phoenix/ Mawrth * | 21.0/20.3/14.4
30 days on the Martian surface at Solar Minimum (worst case for GCR)
Effect of Galactic Cosmic Rays
In “Characterization of the Martian radiation environment on selected locations using the ESA Mars Energetic Radiation Environment Models”, Icarus 218 (2012) 723–734, S. McKenna-Lawlor, P. Gonçalves, A. Keating, B.bMorgado, D. Heynderickx, P. Nieminen, G. Santin, P. Truscot, F. Lei, B. Foing and J. Balaz
15-20 mSv/30 days = 0,5- 0,7 mSv /day
~ < anual limit for Earth radiation workers
~ Daily dose on the ISS

## Slide 26
NASA’s three mission profiles
Short stay
Long stay i), ii)
Comparison
Proposed (2015) by NASA for 2030’s
1 – Short stay
2 – Long stay i)
3 – Long stay ii)
https://nssdc.gsfc.nasa.gov/planetary/mars/marsprof.html (Nov. 2015)

## Slide 27
Dose Calculations
Equivalent doses with shielding are of the same order of astronauts career dose limits
30 days dose limit (deterministic effects): 0.25 Sv  equivalent dose for SEP with shielding is 10% of this value
Stochastic - 3% REID
Results comparison with NCRP/NASA limits

## Slide 28
...it is possible !
28
It is possible to remain in Martian surface for some time with no serious risk for the astronauts!
For longer permanences shelters are required...
Notes: 28

## Slide 29: Jupiter
Beyond the belt

## Slide 30: JUICE ESA L-Mission to the Jovian System

## Slide 31
Slide: courtesy of Insoo Jun (RADECS 2012)

## Slide 32: Very Hard Electron Spectrum
40 MeV
300 keV
Trapped particles:
Main contributor to the Jovian System
Jupiter’s trapped particles are much more energetic than the ones found on Earth
    Jupiter‘s trapped electrons: up to 100MeV
    Jupiter’s trapped protons: up to 1 GeV

## Slide 33: JUICE JUpiter ICy moons Explorer Exploring the emergence of habitable worlds around gas giants
7.6 years cruise &
3.5 years in the Jovian system
14th April 2023

## Slide 34: The radiation environment in the solar system: Jupiter
To Jupiter – ESA Juice Mission (2023): RADEM – RADiation hard Electron Monitor
ESA Contract No. 4000137865/22/ES/JD - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP)
ESA Contact No. 4000110643/13/NL/HB - RADEM Proto-Flight Model (EFACEC, PSI, IDEAS, LIP)

## Slide 35
JUICE Mission

## Slide 36
Europa
Study the emergence of habitable worlds around gas giants
Characterise the Jupiter Icy Moons:
Ganymede, Europa and Callisto as planetary objects and potential habitats
Explore the Jovian system as an archetype for gas giants
Callisto
Ganymede

## Slide 37: RADEM – RADiation hard Electron Monitor
Measurement
electron and proton spectra
ion LET
electron directionality
ESA Contract No. 4000137865/22/ES/JD - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP)
ESA Contact No. 4000110643/13/NL/HB - RADEM Proto-Flight Model (EFACEC, PSI, IDEAS, LIP)

## Slide 38: RADEM – Cruise Phase
May 2024
March 2024

## Slide 39
Cruise phase so far
Credit
M. Pinto

## Slide 40: The radiation environment in the solar system: from Mercury
To Mercury – BepiCOlombo Mission (2018)
BERM – BepiColombo Radiation Monitor
To Jupiter – ESA Juice Mission (2023)
RADEM – RADiation hard Electron Monitor
ESA Contract No. 4000137865/22/ES/JD - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP,SE2S)
ESA Contact No. 4000110643/13/NL/HB - RADEM Proto-Flight Model (EFACEC, PSI, IDEAS, LIP)

## Slide 41: The radiation environment in the solar system: Mercury
ESA BepiColombo Mission (2018): BERM – BepiColombo Radiation Monitor
ESA Contract No. 4000137865/22/ES/JD - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP,SE2S)

## Slide 42
BepiColombo Mission
Understand the origin & evolution of Mercury and its surrounding environment:
The planet closest to the Sun
The only terrestrial planet besides Earth with a self-sustained magnetic field
The smallest planet in our Solar System.
Keyplanet for understanding the evolutionary history of our Solar System and therefore also for the question of how the Earth and our Planetary System were formed.
The scientific objectives focus on a global characterization of Mercury through the investigation of its interior, surface, exosphere, and magnetosphere.
Performe Einstein’s theory of general relativity.

## Slide 43
BepiColombo Mission
First European Mission to Mercury
ESA/JAXA
Radiation Monitoring is a task of the BepiColombo Radiation Monitor (BERM)
Carlota Cardoso, Master’s thesis @LIP/IST July 22

## Slide 44
BERM
BERM stack: 11 silicon sensors
Sensors areas: [0.5; 903] mm2
Sensors thickness: 0.2 mm or 0.3 mm
Absorber layers: aluminium and tantalum
Shield walls: tantalum
Entrance: beryllium cut-off layer and 40º FOV
40º
17.48 cm
12.00 cm
10.60 cm

## Slide 45
SIXS-P
Particle Spectrometer also on board of the MPO
BERM-SIXS SEP Sept 2023

## Slide 46
Cruise phase so far

## Slide 48
INDEX
BERM Proton and Electron data January 2025: 6th Mercury Flyby 6th Jan- 11th Jan
BERM Proton
channels
BERM electron
channels
Time UTC