## Slide 1: Radiation Environment in Space
Luisa Arruda
luisa@lip.pt

## Slide 2
Space Radiation Environment
Van Allen
Radiation Belts
Galactic Cosmic
Radiation (GCR)
Protons and electrons
AP-8 and AE-8 models
p, , O and Fe
ISO 15390
Solar min: 30 Jan 2009
Solar max: 30 Jan 2014
1 AU from Earth
SEP event
Protons
Integrated 14 day SEP event of December 2006

## Slide 3: GCR and Solar cycle activity
Modulation with solar activity – 11 yr cycle
Solar cycle modulated flux inversely proportional to the Sun’s activity
Maximum: solar storms and SEP
Minimum: more GCR
Content available from Living Reviews in Solar Physics
https://www.swpc.noaa.gov/products/solar-cycle-progression
α

## Slide 4: SEP – Solar energetic particles
Associated to
Solar flare
Coronal mass ejections (CME)
Mainly protons and electrons
Energies from several hundred MeV/nuc to GeV/nuc
List from 1976-present @ https://umbra.nascom.nasa.gov/SEP
At Earth's surface, the atmosphere in conjunction with the geomagnetic field provides considerable protection against cosmic rays and solar particle events!
In Space, SEPs are responsible for spacecraft system and component hazard and damage and impose strict constrains on human space exploration.

## Slide 5: SEP - Eventos solares
Notes: Solar Flares are huge explosions on Sun’s surface, usually occuring near sunspots. When the tangled magnetic fields, coming out of the surface, reach a "breaking point", like a rubber band that snaps when wound too tight, huge bursts of energy are released as the field lines reconnect. This can lead to the formation of a Solar flare, as depicted in figure. In the magnetic reconnection process, a huge amount of magnetic energy is rapidly released and transformed to thermal and kinetic energy of the particles. Reconnection can accelerate particles to a high energy (few GeV) within a short time, as required by the very impulsive SEP events. Ejected particles may either remain trapped, or escape into the interplanetary space, if the upper magnetic configuration becomes open. The particles emitted during these kind of events are mainly photons (γ-rays and X-rays), protons and electrons.
CME are quite common during periods of high Solar Activity and are characterized by being spatially larger and temporarily slower than Solar flares. During a CME, huge quantities of plasma, initially trapped in closed coronal magnetic field lines, are ejected into interplanetary space (involving typically 1012 to 1013 kg of mass, and kinetic energies of 1024 to 1025 J).

## Slide 6
Solar Energetic Particle Events
Long term record
More in “maximum” solar activity years
Highly unpredictable
Design for by making a statistical assessment

## Slide 7: The Magnetosphere: an invisible shield
Particles coming from space and produced in their interaction with the atmosphere are trapped by the Earth’s magnetosphere forming the Earth´s radiation belts
In Earth orbits the radiation belts containing trapped electrons and protons constitute the major radiation source

## Slide 8: Earth radiation belts
Particles coming from Space depending on their R may be trapped by the geomagnetic field and form the Earth’s radiation belts.
In Earth’s orbits the radiation belts containing trapped e- and p constitute the major radiation source = dynamic environment
Inner belt (700-10000km)
Dominated by p
Product of CR Neutron Decay
E~100’s MeV
Outer belt (~20000-70000km)
    Dominated by e-
    Controlled by “storms”
Dominates GEO environment & Navigation (Galileo, GPS) orbits & certain Science missions in highly elliptic orbits (XMM-Newton, INTEGRAL)
    E~ MeV

## Slide 9: Earth Radiation Belt Models
protons
Based on data from 1960-1970
Long term averages
but : outer belt is very stormy
ongoing work to update models
Electrons
ISS
Nav
GEO
Examples of models: AP8, AE8 (but there are more…)
electrons

## Slide 10: Aurora
The charged particles trapped in the radiation belts may excite the Earth’s atmosphere N2 and O2 that when return to the fundamental state emit visible radiation.

## Slide 11: Radiation effects in Earth orbits

## Slide 12
The Moon

## Slide 13
The Moon
6:41 p.m. EDT, on April 6, 2026, ARTEMIS II, NASA
No Atmosphere
Very weak localized crustal magnetic field
Radiation environment
SEP and GCR @ 1AU
Albedo neutrons (modulated by H2O)
No radiation belts

## Slide 14
Lunar Radiation Model
ARTEMIS II, NASA
LUNAIRE – LUNar Ionizing Radiation Environment
Primaries: Protons GCR Solar Max
Credits: Bruna Lima

## Slide 15: Mars
Away from home

## Slide 16
Mars Radiation Environment
Corresponds to proton range on Mars atmosphere
Spectral
changes

## Slide 17
Radiation Environment Modelling
17
MarsREM: the Mars Energetic Radiation Environment Models
LIP developed dMEREM, a Geant4 based model for the radiation environment on Mars, Phobos and Deimos, including local treatment of surface topography and composition, atmospheric composition and density (including diurnal + annual variations) and local magnetic fields.
Example of dMEREM results:
Particle radiation arriving on Mars surface after GCR-alpha interaction with atmosphere and soil
Inputs given as a function of latitude, longitude, in a 5º x 5º grid, and season.

## Slide 18
Validation of dMEREM, the Detailed Mars Energetic Radiation Environment Model, with RAD Data from the Surface of Mars
Protons at the surface of Mars September 2017
Protons at the surface of Mars Nov 2015 – Jan 2016
P. Gonçalves L. Arruda, M. Pinto, Front. Astron. Space Sci., 21 February 2022, Sec. Planetary Science

## Slide 19: 30 days on Mars
Mars location | Ambient Dose Equivalent (mSv)
Viking 1/Phoenix/ Mawrth * | 21.0/20.3/14.4
30 days on the Martian surface at Solar Minimum (worst case for GCR)
Effect of Galactic Cosmic Rays
In “Characterization of the Martian radiation environment on selected locations using the ESA Mars Energetic Radiation Environment Models”, Icarus 218 (2012) 723–734, S. McKenna-Lawlor, P. Gonçalves, A. Keating, B.bMorgado, D. Heynderickx, P. Nieminen, G. Santin, P. Truscot, F. Lei, B. Foing and J. Balaz
15-20 mSv/30 days = 0,5 - 0,7 mSv /day
~ < anual limit for Earth radiation workers
~ Daily dose on the ISS

## Slide 20
...it is possible !
20
It is possible to remain in Martian surface for some time with no serious risk for the astronauts!
For longer permanences shelters are required...
Notes: 20

## Slide 21: Jupiter
Beyond the belt

## Slide 22: JUICE ESA L-Mission to the Jovian System

## Slide 23
Slide: courtesy of Insoo Jun (RADECS 2012)

## Slide 24: Very Hard Electron Spectrum
40 MeV
300 keV
Trapped particles:
Main contributor to the Jovian System
Jupiter’s trapped particles are much more energetic than the ones found on Earth
    Jupiter‘s trapped electrons: up to 100MeV
    Jupiter’s trapped protons: up to 1 GeV

## Slide 25: JUICE JUpiter ICy moons Explorer Exploring the emergence of habitable worlds around gas giants
7.6 years cruise &
3.5 years in the Jovian system
14th April 2023

## Slide 26: The radiation environment in the solar system: Jupiter
To Jupiter – ESA Juice Mission (2023): RADEM – RADiation hard Electron Monitor
ESA Contract No. 4000137865/22/ES/JD CCN2 - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP)
ESA Contact No. 4000110643/13/NL/HB - RADEM Proto-Flight Model (EFACEC, PSI, IDEAS, LIP)

## Slide 27
JUICE Mission

## Slide 28
Europa
Study the emergence of habitable worlds around gas giants
Characterise the Jupiter Icy Moons:
Ganymede, Europa and Callisto as planetary objects and potential habitats
Explore the Jovian system as an archetype for gas giants
Callisto
Ganymede

## Slide 29: RADEM – RADiation hard Electron Monitor
Measurement
electron and proton spectra
ion LET
electron directionality
ESA Contract No. 4000137865/22/ES/JD - Expert support to BERM (BepiColombo Environment Radiation Monitor) & RADEM units on board BepiColombo and JUICE spacecraft (LIP)
ESA Contact No. 4000110643/13/NL/HB - RADEM Proto-Flight Model (EFACEC, PSI, IDEAS, LIP)

## Slide 30: RADEM – Cruise Phase
May 2024
March 2024

## Slide 31
LEGA flyby August 2024 RADEM analysis
RADEM @JUICE
Pinto, M., Rodrigues, A., Roussos, E., Schmid, D., Volwerk, M., Kotsiaros, S., Brown, P., Dougherty, M., Arruda, L., and Witasse, O.: RADEM observations of the Van Allen belts during the JUICE Lunar-Earth Gravity Assist, EGUsphere [preprint], https://doi.org/10.5194/egusphere-2026-2055, 2026. (submitted, under discussion)
RADEM can measure energetic electrons, successfully!

## Slide 32
Cruise phase so far
Credit
M. Pinto

## Slide 33
Mercury
M
U
e
r
Y
c
r

## Slide 34
BepiColombo Mission
Understand the origin & evolution of Mercury and its surrounding environment:
The planet closest to the Sun
The only terrestrial planet besides Earth with a self-sustained magnetic field
The smallest planet in our Solar System.
Key planet for understanding the evolutionary history of our Solar System and therefore also for the question of how the Earth and our Planetary System were formed.
The scientific objectives focus on a global characterization of Mercury through the investigation of its interior, surface, exosphere, and magnetosphere.
Perform tests on Einstein’s theory of general relativity.

## Slide 35
BepiColombo timeline

## Slide 36
BepiColombo Mission
First European Mission to Mercury
ESA/JAXA
Radiation Monitoring is a task of the BepiColombo Environment Radiation Monitor (BERM)

## Slide 37
BERM
BERM stack: 11 silicon sensors
Sensors areas: [0.5; 903] mm2
Sensors thickness: 0.2 mm or 0.3 mm
Absorber layers: aluminium and tantalum
Shield walls: tantalum
Entrance: beryllium cut-off layer and 40º FOV
40º
17.48 cm
12.00 cm
10.60 cm

## Slide 38
SIXS-P
Particle Spectrometer also on board of the MPO
BERM-SIXS SEP Sept 2023

## Slide 39: BERM + Artemis II
BepiColombo during Artemis II → privileged position between Earth and the Sun to provide valuable space weather forecasting relevant to crew safety and spacecraft electronics performance.
  COSMOS Heliospheric Conditions at BepiColombo - BepiColombo - Cosmos
BERM measurements used to provide ARTEMIS II support, requested by NASA
Earthset observed from Artemis II. Credit: NASA.
For BERM data: "We acknowledge the use of data from the BERM instrument provided by the Laboratory for Instrumentation and Experimental Particle Physics, funded by ESA and FCT, onboard the ESA/JAXA BepiColombo mission."

## Slide 40
Cruise phase is over: next stop Mercury! But…

## Slide 41: SpaceRad @LIP
Marco Pinto
Tiago Neves
Tiago Neves
André Rodrigues
Rafael Parente
Inês Rosa
Luísa Arruda
Bernardo Tomé
Pedro Assis
Patrícia Gonçalves
António Gomes
Bruna Lima
Magda Soares
Filipe Rodrigues
Isabel Dias
Marta Semblano

## Slide 42: Backup slides

## Slide 43: Solar Wind
Continuous flux of charged particles from the Sun ~400km/s
  mainly e- and p (E~0.5MeV)
  ~1012 particles/m2.s
~4 days to reach the Earth (1UA).
First continuous observation by spacecraft Mariner 2 (1962).
Detailed measurement by spacecraft Ulysses (3 orbits).
“Swepts” the solar magnetic field to IP space

## Slide 44: Solar Magnetic Field
α
α
Sun rotation period ~27.26 days
( Carrington rotation – started 9 Nov 1853)
Magnetic field and magnetic poles approach a dipole.
Continuous Shift between the Sun rotation axis and the magnetic field direction when solar activity comes from Min to Max.
Complex configuration during Solar Max.
Polarity reverses each 11 yrs, returning to its original configuration every 22 years

## Slide 45
NASA’s three mission profiles
Short stay
Long stay i), ii)
Comparison
Proposed (2015) by NASA for 2030’s
1 – Short stay
2 – Long stay i)
3 – Long stay ii)
https://nssdc.gsfc.nasa.gov/planetary/mars/marsprof.html (Nov. 2015)

## Slide 46
Dose limits for exposed classes
Astronauts dose restrictions
NCRP dose limits used by NASA
G. Dietze et al. Assessment of Radiation Exposure of Astronauts in Space. Technical report, The International Commission on Radiological Protection, 2013.
Space Flight Human-System Standard – Volume 1, Revision A: Crew Health, NASA Technical Standard, NASA-STD-3001. Technical report, NASA, 2015.
In 2022, NASA adopted a new unified standard of 0.6 Sv as the career limit for all astronauts, regardless of age and sex, to promote equity.
https://www.nationalacademies.org/read/26155/chapter/1
Notes: Equity concerns — The previous age/sex-based system effectively limited career opportunities for women and younger astronauts, who had lower permissible doses and therefore fewer or shorter missions available to them.
BFO - No adulto, a medula óssea vermelha (encontrada em ossos como o esterno, costelas, vértebras, pélvis e epífises dos ossos longos) é o principal órgão hematopoiético.
No feto, o fígado e o baço desempenham um papel central na produção de sangue.
Em certas doenças (como mielofibrose), o baço e o fígado podem retomar a hematopoiese — processo chamado hematopoiese extramedular.